## Slide 1
WIFI-CSI PRESENCE COLLECTOR — MAIN BRANCH
The Actual Shipped Model:
WhoFi Transformer + Empty-Room Calibration
Not the Random Forest “home model” and not the Signature+EVM open-set experiment — both of
those are later, uncommitted work. This is what's actually merged into main.
ml/models/transformer_whofi.py — train_final_model.py / train_day3_ch6_model.py — live_infer.py
WiFi-CSI Presence Collector — Main-Branch Model (WhoFi Transformer)
1

## Slide 2
OVERVIEW
What's actually on main: one transformer, four tasks
• Model: WhoFiTransformer — a replica of WhoFi (arXiv:2507.12869): 1-layer transformer over amplitude only, mean-pooled, L2-normalized, then a linear classifier head
• Trained independently as a plain closed-set classifier for each of 4 binary tasks (cross-entropy loss, not contrastive) — there is no open-set / EVM layer on main
  – task0_presence: EMPTY vs OCCUPIED
  – taskD_auth_vs_nonauth: NOT AUTHORIZED vs AUTHORIZED (the “auth gate”)
  – taskE_motion_standing_vs_walking: STANDING vs WALKING
  – taskB_identity (legacy, ANJALI vs BARATH): kept because it was asked for, but tested BELOW CHANCE cross-day (AUROC 0.20–0.31) — live_infer.py marks it experimental/unreliable
• Preprocessing: per-day empty-room self-calibration (“calibA”) — z-score every window against that day's own quiet-room baseline before the transformer ever sees it
• Trained on ALL of Day1+Day2 pooled data, no held-out split — Day3 live testing is the real test (train_day3_ch6_model.py later added its own Day3+Day4-only checkpoint track)
• Served by ml/inference/live_infer.py: live calibration → rolling 200-packet windows → per-task prediction → ~30s rolling aggregate, which is the number to trust
WiFi-CSI Presence Collector — Main-Branch Model (WhoFi Transformer)
2

## Slide 3
FLOWCHART
Raw packets → preprocessing → transformer → live decision
Raw CSI packet
ragged csi_len, per-802.11-frame-type
Decode
amp=hypot(re,im)
phase=atan2(im,re)
Subcarrier resample
Day1 186-sub, Day2 128-sub
→ shared 128-sub grid
calibA calibration
z = (x − μ_empty_day) / σ_empty_day
amplitude + phase
Windowing
200-packet window,
100-packet stride (50% overlap)
WhoFiTransformer
1-layer self-attention
→ 32-d embedding
4 independent linear classifier heads (one per task, same shared architecture)
Presence
EMPTY / OCCUPIED
Auth gate
AUTH / NOT AUTH
Motion
STAND / WALK
Identity*
ANJALI / BARATH
Live: ~30s rolling aggregate across overlapping windows — the number to trust
* taskB identity tested below chance cross-day — shown for completeness, not trusted
WiFi-CSI Presence Collector — Main-Branch Model (WhoFi Transformer)
3

## Slide 4
RAW DATA
Decoding the ragged CSI wire format
• samples.npz stores CSI as a flat, ragged buffer — csi_len varies by 802.11 frame type (legacy/HT, 20/40 MHz), so packets are bucketed by csi_len before decoding
• Each subcarrier is one (imag, real) int8 pair; decode is vectorized per bucket (gather + reshape), not a per-packet Python loop
• amplitude = hypot(real, imag) = sqrt(real² + imag²)
• phase = arctan2(imag, real)
• Day 1 sessions negotiated 40 MHz → dominant bucket is 186 subcarriers (372 bytes)
• Day 2 (and Day 3) sessions negotiated 20 MHz → dominant bucket is 128 subcarriers (256 bytes)
• Only the per-session dominant csi_len bucket is kept (~1–6% of minority-shape packets dropped) so every window has one consistent subcarrier count
Shape mismatch across days
Day 1
40 MHz
186 subcarriers
Day 2 / Day 3
20 MHz
128 subcarriers
resample onto shared 128-sub grid
downsample Day1 only — never fabricate Day2's missing resolution
Why 128, not 186: resampling always shrinks toward the smaller native width so both days become shape-compatible for one shared model — upsampling Day 2 would invent detail the hardware never captured.
WiFi-CSI Presence Collector — Main-Branch Model (WhoFi Transformer)
4

## Slide 5
PREPROCESSING
calibA — per-day empty-room self-calibration
Per subcarrier, applied to both amplitude and phase:
x' = ( x − μ_empty ) / ( σ_empty + ε )
• μ_empty, σ_empty are fit once per day from that day's own “none” (empty-room) sessions — amplitude and phase each get their own per-subcarrier mean/std
• Why per-day, not global: this is the direct analog of OpenCSI's Z-score approach (arXiv:2607.26665), which reported F1 0.99 vs 0.87 for cross-room/cross-hardware transfer on ESP32 — tested here for person-ID/auth for the first time
• Live inference computes the same baseline on the fly: a 15s “stand outside the room” calibration phase at the start of every session (ml/inference/live_calibration.py), reusing the exact same DayBaseline math and apply_variant_a() function as the offline training pipeline
• Two alternatives were tried and NOT used as the default:
  – Variant B (cross-day re-referencing onto a fixed reference day) — underperforms calibA, likely because it assumes the empty-vs-occupied relationship transforms identically across days
  – ℓ₁ per-packet gain normalization — implemented and unit-tested, not yet run through the full sweep
• Net effect measured (see results slide): calibA trades some raw AUROC for a much lower false-accept rate against a genuine stranger — the metric that actually matters for the auth task
WiFi-CSI Presence Collector — Main-Branch Model (WhoFi Transformer)
5

## Slide 6
PREPROCESSING
Windowing — turning a packet stream into fixed-size inputs
Calibrated stream
(N packets, 128 subcarriers)
amplitude + phase
Slide a window
window_packets = 200
(~1s at ~200Hz observed rate)
Stride forward
stride_packets = 100
(50% overlap)
Model input
(200, 128)
per window
• Observed packet rate on the dominant bucket: 162–263 Hz (mean ~217 Hz) across Day1 sessions — so 200 packets is close to a 1-second window, matching the ESP32 person-ID paper's convention
• The live rolling windower (ml/inference/live_window.py) mirrors this exactly, so a live window is the same shape a checkpoint was trained on — the very first window is ready as soon as the buffer first fills, not after one extra stride's delay
• Per-session caching avoids re-decoding: each session's dominant-bucket arrays are decoded once and memory-mapped, so building thousands of overlapping windows stays cheap
• train_day3_ch6_model.py's later checkpoint track adds one more step before windowing: bin-average resampling of the TIME axis onto a common packet rate, to stop window duration from correlating with whichever label happened to be recorded at a different network congestion level
WiFi-CSI Presence Collector — Main-Branch Model (WhoFi Transformer)
6

## Slide 7
MODEL ARCHITECTURE
WhoFiTransformer — single amplitude branch + linear head
Input: amplitude (B, T=200, S=128)
BranchEncoder: Linear 128→32 + positional encoding
Transformer encoder × 1
(self-attn → Add&Norm → FFN → Add&Norm)
Mean-pool over time → (B, 32)
signature_module: Linear 32→32, L2-normalize
classifier: Linear 32→n_classes (per task)
Output: logits (B, n_classes)
Notes on this exact architecture
• Amplitude only, no phase branch — matches WhoFi's own published design; phase is accepted by forward() for a uniform call signature across the model zoo but is otherwise ignored
• d_model=32, 4 heads, d_ff=64, 1 layer — WhoFi's own ablation found 3 layers unstable/worse on a dataset this small, so the shallow config is the deliberate winner, not a placeholder
• signature_module (Linear 32→32 + L2-normalize) produces an embedding shaped like a verification “signature”, but on main it feeds straight into a plain linear classifier — there's no contrastive loss or EVM open-set layer wired up here (that's the later, uncommitted signature+EVM experiment)
• One separate model instance is trained per task (presence / auth / motion / identity) — same architecture and hyperparameters, four independent checkpoints, not a shared multi-head model
• classifier is a single nn.Linear(32, n_classes) — as simple as the architecture gets after the transformer; all the representational work happens in the 1-layer encoder
WiFi-CSI Presence Collector — Main-Branch Model (WhoFi Transformer)
7

## Slide 8
TRANSFORMER INTERNALS
Scaled dot-product multi-head self-attention
Per head:
Attention(Q, K, V) = softmax( Q Kᵀ / √d_k ) V
Q, K, V are learned linear projections of the 32-dim per-packet token sequence; d_k = d_model / n_heads = 32 / 4 = 8 here.
• Each of the 200 packets in a window becomes one 32-dim token via the input projection
• 4 heads run attention in parallel, then concatenate — each head can latch onto different subcarrier/time relationships across the window
• Post-LN block structure (this repo's default):
  – x = LayerNorm( x + Dropout( SelfAttention(x) ) )
  – x = LayerNorm( x + Dropout( FFN(x) ) )
• Sinusoidal positional encoding, added elementwise to the projected input:
  – PE(pos, 2i) = sin( pos / 10000^(2i/d_model) )
  – PE(pos, 2i+1) = cos( pos / 10000^(2i/d_model) )
• Mean-pool collapses the 200 refined tokens to one (B, 32) vector per window
• L2-normalize (signature_module output): s = z / ‖z‖₂ → ‖s‖ = 1 — used here only as an internal representation before the linear classifier, not for distance-based matching (no EVM on main)
WiFi-CSI Presence Collector — Main-Branch Model (WhoFi Transformer)
8

## Slide 9
TRAINING
Four independent binary classifiers, one recipe
• Loss: plain torch.nn.CrossEntropyLoss — closed-set classification, not contrastive/in-batch-negative (that loss exists in ml/training/losses.py but is not what trains the shipped checkpoints)
• Optimizer: Adam, lr=1e-3, batch_size=64, seed fixed and logged per run
  – Why the seed matters: re-training the SAME model on the SAME fold gave wildly different results (taskD fold 1: AUROC 0.757 vs 0.698, false-accept-unauthorized 26% vs 57%, across two otherwise-identical runs) — on a dataset this small with only a handful of epochs, seed variance can be as large as the effect being measured
• Deployable checkpoints (train_final_model.py): trained on ALL Day1+Day2 pooled data, the SAME dataset passed as both train and test — deliberate, not an oversight
  – The printed accuracy is an in-sample sanity check only, never a generalization estimate — carving out an internal validation slice would reintroduce the 50%-overlapping-window leakage problem session-disjoint splitting exists to prevent
  – Day 3, tested live via live_infer.py, is the real held-out test
• Later track (train_day3_ch6_model.py): honest numbers come FIRST — leave-one-unauthorized-person-out for the auth task, session-disjoint 80/20 for presence/motion — THEN a final checkpoint is retrained on 100% of that track's data, so the two-stage “evaluate honestly, then ship” discipline is consistent across both checkpoint generations
WiFi-CSI Presence Collector — Main-Branch Model (WhoFi Transformer)
9

## Slide 10
LIVE INFERENCE
live_infer.py — from board stream to a trusted decision
Bandwidth/channel gate
checked BEFORE the calibration
wait — fail fast on wrong config
Live calibration
~15s “stand outside
the room” → empty-room baseline
Rolling window
200-packet window,
100-packet stride
4 task predictions
instantaneous
probability per task
~30s rolling aggregate
mean over ~60 windows —
the number to trust
• Presence gates the display of Auth/Motion: if the aggregate presence probability says “empty”, Auth and Motion print “n/a (no one present)” rather than a misleading guess
• Guided phases (optional): prompts + a live countdown for “STAND STILL” then “WALK AROUND”, so a tester knows exactly when to switch — Auth doesn't need this split, Motion does
• Time-normalized checkpoints (the day3ch6 track) additionally bin-average the raw live packet stream onto the training-time target rate before windowing, via LiveTimeResampler — otherwise the exact packet-rate confound the offline fix closed would reappear live
• A periodic bandwidth re-check runs every 3000 packets during streaming — warns rather than aborts, since aborting a live demo mid-flight over a possibly-transient blip is worse than a warning
WiFi-CSI Presence Collector — Main-Branch Model (WhoFi Transformer)
10

## Slide 11
VALIDATED RESULTS
raw vs. calibA, and why aggregation window length matters
Preprocessing | n_windows | Accuracy | AUROC | False-accept unauth. | False-accept none
raw | 60 (~30s) | 0.798 | 0.899 | 58.2% | 3.9%
calibA | 60 (~30s) | 0.749 | 0.821 | 5.5% | 1.6%
Calibration and aggregation window length are COMPOUNDING levers — false-accept-unauthorized under calibA shrinks monotonically as the window lengthens:
21.5%
1 window
(~1s)
13.7%
~5s
13.0%
~10s
8.0%
~20s
5.5%
~30s
Recommended production config: whofi_transformer + calibA + ~30s decision window.
Raw's peak AUROC is higher (0.899 vs 0.821), but that's the wrong number to optimize for this task — calibA is dramatically better at the decision that actually matters: correctly rejecting a real intruder.
WiFi-CSI Presence Collector — Main-Branch Model (WhoFi Transformer)
11

## Slide 12
KNOWN LIMITATIONS
Read this before demoing it
• taskB (identity, anjali/barath) tested BELOW CHANCE cross-day — AUROC 0.20–0.31, where 0.5 is a coin flip. Included because it was asked for; live_infer.py labels its output experimental/unreliable
• Day1 (186-sub, 40 MHz) vs Day2/3 (128-sub, 20 MHz) were captured on non-overlapping RF frequency bands — resampling + calibA compensate, but router channel/bandwidth pinning before future collection days is still the field's actual recommended fix, not a purely algorithmic one
• calibA requires a fresh per-day (or per-session, live) empty-room baseline — a brand-new environment with no quiet-room recording has no calibration to apply
• Deployable checkpoints have zero internal held-out split by design — their printed accuracy is a sanity check, not a generalization estimate; only the separate sweep runs and Day3 live testing are the trustworthy numbers
• Explicitly ruled out or not fully wired in yet:
  – CSI-ratio method (cancel phase noise via 2 Rx antennas) — needs 2+ antennas; this ESP32-S3 setup is 1x1, not applicable
  – ℓ₁ per-packet gain normalization — implemented, unit-tested, not yet run through the full sweep as a real comparison arm
  – RSSI fusion — implemented as a non-invasive wrapper, verified on a small smoke sample only, not a full sweep arm
  – Doppler/velocity-domain features — the most cross-day-robust representation found so far in exploratory work (AUROC never flips below chance in either direction), but needs a much longer 10–18s decision horizon and isn't part of the shipped pipeline
WiFi-CSI Presence Collector — Main-Branch Model (WhoFi Transformer)
12

## Slide 13
FOR CONTEXT
How this relates to the other (uncommitted) approaches
 | Main branch (this deck) | Home Model (RF) | Signature + EVM
Committed to main? | Yes | No — local/uncommitted | No — local/uncommitted
Model | WhoFiTransformer (1-layer) | Random Forest, 300 trees | Transformer + Weibull/EVM
Tasks | Presence, Auth-gate, Motion, Identity (unreliable) | Closed 2-class identity only | Open-set accept/reject + ID
Calibration | calibA (empty-room z-score) | None needed (RF invariant) | None (found harmful here)
Status | Deployed / validated | Experimental | Experimental
WiFi-CSI Presence Collector — Main-Branch Model (WhoFi Transformer)
13