## Slide 1
WIFI-CSI PRESENCE COLLECTOR
CSI Preprocessing Pipeline &
Transformer Architecture
How raw WiFi Channel State Information becomes clip / window features, and how the
signature transformer (BranchEncoder) consumes and manipulates that data.
Current branch — Home Model (Random Forest) + Signature/EVM (Transformer)

## Slide 2
OVERVIEW
Two model families live on this branch
Same raw CSI source, two unrelated pipelines and feature representations.
HOME MODEL (v2, deployed)
• Task: closed 2-class identity — anjali vs barath, always picks one
• Model: Random Forest, 300 trees, class_weight="balanced"
• Features: 4 statistical moments (mean/std/skew/kurtosis) per subcarrier
• Windowing: 3 s clips, 1 s stride, 50% coverage gate
• Feature vector: 4 × 128 subcarriers = 512 numbers per clip
• No neural network anywhere in this path
• Same-day accuracy ~70–95%; cross-day ~55–70%
SIGNATURE + EVM (experimental, open-set)
• Task: open-set accept/reject — can say “unknown”, plus identify
• Model: Transformer encoder (BranchEncoder) → 32-d signature
• + Extreme Value Machine (Weibull tails) for the accept/reject decision
• Features: raw amplitude sequence — no hand-engineered moments
• Windowing: 200-packet windows, 100-packet stride (50% overlap)
• Trained with in-batch-negative contrastive loss (WhoFi-style)
• Mean AUROC ≈ 0.45 across held-out strangers — experimental, not deployed
WiFi-CSI Presence Collector — Pipeline & Model Architecture
2

## Slide 3
FLOWCHART
End-to-end: raw packets → preprocessing → both pipelines
Raw CSI packets
~100–150 pkt/s, 128 complex subcarriers
Clean
drop bad packets
Dominant length
keep mode csi_len
Amplitude
sqrt(real²+imag²)
HOME MODEL — Random Forest
SIGNATURE + EVM — Transformer
Clip windowing (3 s / 1 s stride) + 50% coverage gate
Per-subcarrier moments: mean, std, skew, kurtosis
Feature vector: 4 × 128 subcarriers = 512-d
Random Forest — 300 trees, bagging + feature subsampling
Majority vote across clips → anjali / barath
Time-normalize: resample to common packet rate
Windowing: 200-packet windows / 100-packet stride
Transformer encoder (BranchEncoder): attention → 32-d
Mean-pool + L2-normalize → unit-norm signature
EVM Weibull scoring → accept/reject + identity / “unknown”
WiFi-CSI Presence Collector — Pipeline & Model Architecture
3

## Slide 4
RAW DATA
What a CSI reading actually is
• Every WiFi packet the ESP32 hears yields one CSI reading
• The channel is split into ~128 narrow frequency slices (subcarriers)
• Each subcarrier's CSI value is a complex number: real + imaginary part
• Packets arrive continuously — roughly 100–150 packets/second
• Amplitude is used, not phase:
  – amplitude = sqrt(real² + imaginary²)
  – Phase is noisy on cheap radios (ESP32 clock/sampling offsets) —
  – amplitude is the standard, more robust channel for this kind of sensing
One packet → one CSI vector
WiFi packet
128 complex
subcarriers
one CSI reading
amplitude = |real + i·imag|
sqrt(real² + imag²), per subcarrier
A full session = a stream of these amplitude vectors over time —
variable length, noisy, not directly usable by a fixed-input model.
WiFi-CSI Presence Collector — Pipeline & Model Architecture
4

## Slide 5
PREPROCESSING
Raw session → clean amplitude timeline
Shared by both pipelines before they diverge into clip-moments (Home Model) vs raw windows (Signature model).
Raw packets
per-session CSI stream
Clean
drop first_word_invalid +
duplicate-timestamp packets
Dominant length
keep the mode csi_len;
drop odd-shaped frames
Amplitude
sqrt(real²+imag²)
per subcarrier, per packet
Then the two pipelines diverge:
• Home Model: cut into 3 s / 1 s-stride clips → reduce each clip to 4 moments per subcarrier
• Signature model: resample to a common packet rate → cut into 200-packet windows, fed raw to the transformer
WiFi-CSI Presence Collector — Pipeline & Model Architecture
5

## Slide 6
HOME MODEL PIPELINE
Clip windowing → statistical moments
Clip windowing
3.0 s clips, 1.0 s stride
(67% overlap)
Coverage gate
drop clip if
< 50% expected packets
Per-subcarrier moments
mean, std, skew,
excess kurtosis
Feature vector
4 × 128 subcarriers
= 512 numbers
The four moment formulas (per subcarrier, over all N amplitude samples in a clip):
• Mean: μ = (1/N) Σ xᵢ
• Std dev (population): σ = sqrt( (1/N) Σ (xᵢ − μ)² )
• Skewness (Fisher–Pearson): skew = (1/N) Σ (xᵢ − μ)³ / (σ³ + ε) — asymmetry of the fade pattern
• Excess kurtosis (Fisher): kurt = (1/N) Σ (xᵢ − μ)⁴ / (σ⁴ + ε) − 3 — spikiness from motion
• ε = 1e-6 guards divide-by-zero on constant subcarriers; resulting NaNs → 0
WiFi-CSI Presence Collector — Pipeline & Model Architecture
6

## Slide 7
HOME MODEL
Random Forest classifier + session vote
• 300 decision trees, class_weight="balanced"
  – Bagging: each tree trains on an independent bootstrap resample of clips
  – Feature subsampling: each split only considers sqrt(512) random features
  – Split rule: Gini impurity reduction, Gini = 1 − Σ pₖ²
  – Prediction: majority vote across all 300 trees, per clip
• No empty-room calibration needed
  – RF splits are threshold tests — invariant to affine (z-score) rescaling,
  – so raw clip moments are used directly
• Session-level output = majority vote across all overlapping clips
  – smooths out noisy, correlated per-clip guesses, like averaging many weak estimates
512-d clip feature vector
300 decision trees
bagging + random feature subsets
per-clip prediction + confidence
session-level majority vote
WiFi-CSI Presence Collector — Pipeline & Model Architecture
7

## Slide 8
SIGNATURE MODEL PIPELINE
Preprocessing before the transformer
Session pool
Day3+Day4,
channel-6-only
Time normalization
resample to a common
packet rate (bin-average)
Windowing
200-packet windows,
100-packet stride
No calibration
raw amplitude,
no empty-room z-score
• Why time-normalize: different sessions/days have slightly different native packet rates — without this a model could learn to distinguish sessions by packet density instead of CSI content
• Why windows, not moments: a transformer already has attention to summarize a sequence itself, so it is given the raw amplitude sequence rather than a hand-reduced feature vector
• Why no calibration: the reference project tested empty-room z-scoring for this contrastive setup and found it neutral-to-harmful — it let the model implicitly answer “is this authorized data” instead of learning identity signal directly
• Amplitude only, no phase — same reasoning as the home model (matches WhoFi's published design choice)
• Trained on all 8 recorded identities (anjali, barath + 6 strangers) so the open-set boundary has impostor examples to reject against
• Input shape to the encoder: (batch, T=200, n_subcarriers=128)
WiFi-CSI Presence Collector — Pipeline & Model Architecture
8

## Slide 9
TRANSFORMER ARCHITECTURE
BranchEncoder — how it consumes CSI data
Input: amplitude (B, T=200, S=128)
Linear projection: 128 → d_model=32
+ Sinusoidal positional encoding
Transformer encoder layer × 1
(self-attn → Add&Norm → FFN → Add&Norm)
Mean-pool over time: (B,T,32) → (B,32)
Linear 32→32, then L2-normalize
Output: unit-norm signature (B, 32)
What each stage does to the CSI window
• Input projection — each packet's 128-subcarrier amplitude vector becomes one 32-dim “token”; 200 packets = 200 tokens in the sequence
• Positional encoding — attention has no notion of order by itself, so a sinusoidal pattern is added per position so the model can tell packet 1 from packet 150
• Self-attention — every packet-token looks at every other packet-token in the window and reweights itself by how relevant they are to each other (see next slide for the math)
• Feed-forward network — a small per-token MLP (32→64→32) applied identically to every token, adding non-linear capacity after attention mixes information across time
• Mean-pool — collapses the 200 refined tokens into a single 32-d vector per window, a simple parameter-free way to summarize a variable-length window
• L2-normalize — projects the embedding onto the unit hypersphere so distance and cosine similarity between two people's signatures become directly comparable
WiFi-CSI Presence Collector — Pipeline & Model Architecture
9

## Slide 10
TRANSFORMER INTERNALS
Scaled dot-product multi-head self-attention
Per head:
Attention(Q, K, V) = softmax( Q Kᵀ / √d_k ) V
Q, K, V are learned linear projections of the 32-dim token sequence; d_k = d_model / n_heads = 32 / 4 = 8 here.
• 4 heads run this in parallel, then concatenate — each head can latch onto different subcarrier-amplitude relationships across the window
• Post-LN block structure (this repo's default):
  – x = LayerNorm( x + Dropout( SelfAttention(x) ) )
  – x = LayerNorm( x + Dropout( FFN(x) ) )
• d_model=32, 1 layer, 4 heads is deliberately small — both the WhoFi paper and the ESP32 person-ID paper found going deeper hurt on datasets this small (thousands of windows, not millions)
• Sinusoidal positional encoding, added elementwise to the projected input:
  – PE(pos, 2i) = sin( pos / 10000^(2i/d_model) )
  – PE(pos, 2i+1) = cos( pos / 10000^(2i/d_model) )
• L2 normalization at the output:
  – s = z / ‖z‖₂ → ‖s‖ = 1
  – makes Euclidean distance and cosine similarity monotonically related:
  – ‖a−b‖² = 2 − 2·cos(a,b) for unit vectors a, b
WiFi-CSI Presence Collector — Pipeline & Model Architecture
10

## Slide 11
TRAINING OBJECTIVE
In-batch-negative contrastive loss (DPR / WhoFi-style)
• PK-sampling: every identity with ≥2 windows contributes one (query, gallery) pair per step
• Query and gallery windows are drawn from different (date, motion) contexts when available
  – Why: a diagnostic found the encoder otherwise learning to separate recording-session
  – context instead of identity — forcing cross-context pairs makes the loss only
  – satisfiable by identity signal that survives a context change
• Loss (cosine-similarity matrix over the batch, cross-entropy on the diagonal):
sim = Sq · Sgᵀ ∈ ℝ^(B×B) (dot product of L2-normalized query/gallery batches)
L = −(1/B) Σᵢ log( exp(simᵢᵢ) / Σⱼ exp(simᵢⱼ) )
Every other identity in the batch is a free “in-batch negative” — no separate negative-mining step needed. Adam optimizer, lr=1e-3, 300 epochs × 40 steps/epoch, seed=0.
WiFi-CSI Presence Collector — Pipeline & Model Architecture
11

## Slide 12
OPEN-SET DECISION
Extreme Value Machine (EVM) turns embeddings into accept/reject
Signature embedding (32-d)
unit hypersphere
Weibull tail per identity
fit on nearest-τ distances
ψ-score → accept/reject
threshold = 0.18
• Why not a plain classifier: a closed-set softmax structurally cannot say “none of these” — measured 68.5% false-accept rate against a genuinely novel stranger
• EVM idea (Extreme Value Theory): the distance from a point to another class's points behaves like an extreme-value statistic — modeled here as a Weibull tail per support point
• Score: ψ(x, point) = exp( −(‖x − point‖ / λ)^k ) — the Weibull survival function, used as an inclusion/similarity score (1 at zero distance, decaying with distance)
• This run uses centroid_only=True: each identity collapses to one centroid before fitting (per-point EVM was noisier with only ~289 points per identity)
• Final accept score = top-5-averaged ψ across an identity's support points, max over enrolled identities
• Honest result: mean AUROC ≈ 0.45 across held-out strangers — experimental, not deployed; the home model (Random Forest) remains the shipped path
WiFi-CSI Presence Collector — Pipeline & Model Architecture
12

## Slide 13
SUMMARY
Home Model vs Signature + EVM, side by side
 | Home Model (v2) | Signature + EVM
Task | Closed 2-class ID (anjali/barath) | Open-set accept/reject + ID
Model | Random Forest (300 trees) | Transformer encoder (32-d) + Weibull/EVM
Input to model | 512-d per-clip moment vector | Raw (T=200, 128-sub) amplitude sequence
Windowing | 3 s clips / 1 s stride, 50% coverage gate | 200-packet windows / 100-packet stride
Calibration | None (RF invariant to affine rescale) | None (found harmful for this setup)
Can say “unknown”? | No | Yes
Status | Deployed | Experimental
WiFi-CSI Presence Collector — Pipeline & Model Architecture
13

## Slide 14
LIMITATIONS & NEXT STEPS
What this pipeline does not do yet
• Home model only knows 2 people — a stranger still gets forced into anjali or barath
• Day3→Day4 was never isolated/cross-validated before v2 shipped — it pools both days
• Sensitive to WiFi channel — trained only on channel 6 / 20 MHz
• Signature+EVM false-accept rate is still too high for anything beyond experimentation
• No cross-day validation beyond Day3+Day4 for the signature model (no Day5 yet)
• Documented next levers for EVM (not bugs, just not built yet):
  – Cohort / T-norm score normalization — biggest false-accept-rate reducer in the reference project
  – Per-identity EER thresholds instead of one global 0.18
  – Multi-seed ensembling
  – Walking-motion gating
  – Temporal smoothing over consecutive windows
WiFi-CSI Presence Collector — Pipeline & Model Architecture
14